## Slide 1: Wired Communication
By: Haron Abdel-Raziq

## Slide 2: Schedule & Other Details
We noticed the struggle with Lab 2
  Lab 2 is now due on October 5th
  Milestone 2 is Due on October 12th
Next week (Monday) there is an FPGA lecture
  Will be given by Professor Bruce Land
  You should definitely attend

## Slide 3: Wired Communication

## Slide 4: Why Wired?
Wired connectivity is by far the most prevalent type of interconnection on chip
Important to understand how it functions if you intend on combining many chips together on a single board
Allows for a wide variety of interfaces
Reliable, fast, relatively straightforward to implement/understand

## Slide 5: Parallel Vs. Serial
Parallel
Serial
Sending Bit Pattern 01000011

## Slide 6: Parallel Vs. Serial
Serial
  Pros
    Simpler design (fewer wires and pins)
    Can be clocked faster than parallel
    Can be asynchronous
  Cons
    Sends a single stream of data
Parallel
  Pros
    Transmit data over multiple channels simultaneously
  Cons
    Must always be clocked
    Requires more wires and pins
    Crosstalk
    Intersymbol Interference (ISI)
PCI: Max Parallel Speed: 4.266 Gbits/s, Max Serial Speed: 256 Gbits/s

## Slide 7: Serial Communication
 | UART | SPI | I2C
Maximum Speed | 115200b/s | 10 Mbps | 5 Mbps
Synchronous/ Asynchronous | Asynchronous | Synchronous | Synchronous
# Of Wires | 2 | 4 | 2
Max # of Masters | 1 | 1 | Unlimited
Max # of Slaves | 1 | Unlimited* | 1008

## Slide 8: SPI (Serial Peripheral Interface)
Master sends data on MOSI line
Clocked by SCLK
One bit per clock cycle
Configurable clock
Multiple slaves controlled by SS/CS (active low)
Commonly used for: memory, memory cards, sensors, displays
MOSI = Master Out/Slave In
MISO = Master In/Slave Out
SCLK = Serial Clock
SS/CS = Slave/Chip Select

## Slide 9
Master
Outputs Clock
Signal
Master
Switches SS/CS Low
Slave Is Activated
Master
Sends Data One Bit At A Time
Slave Reads Bits As They Are Received
Slave Responds Along MISO
Master Reads One Bit At a Time

## Slide 10: SPI
Advantages
  Stream bits (unlimited frame)
  High speed
  Send & receive lines
Disadvantages
  No error checking
  No acknowledgement
  Requires four wires
  Single master

## Slide 11: SPI
Team Alpha implemented SPI communication to their FPGA
Check out their website for Lab 4
https://cei-lab.github.io/ECE3400-2017-teamAlpha/lab4.html

## Slide 12: UART (Universal Asynchronous Receiver/Transmitter)

## Slide 13: UART
A UART is a physical IC (sometimes contained as part of an MCU)
Two wire communication
Converts incoming parallel data to serial, transmits, converts back
Asynchronous
  But there is an agreed upon baud rate
  Start bit signals when reading begins
  Use a particular “packet” format

## Slide 15: UART
Commonly Used For
  GPS Modules
  Bluetooth Modules
  RFID Card Reader Modules
Advantages
  Widely used
  Requires only two wires
  Asynchronous
  Parity bit for error checking
Disadvantages
  Fixed packet size
  Single Master/Slave
  Baud rates must be within 10%

## Slide 16: I2C (Inter Integrated Circuit)
Inter Integrated Circuit combines SPI and UART benefits
  Multiple masters and multiple slaves
  2 wires
Start Condition: SDA High to Low before SCL High to Low
Stop Condition: SDA Low to High after SCL High to Low

## Slide 17: I2C Configurations

## Slide 18
Start Condition Is Sent
Address is Sent

## Slide 19
ACKnowledgement Sent
(Pull SDA Line Low)
Master Sends or Receives Data

## Slide 20
After Each Data Frame
An ACK/NACK is Sent
Master Sends Stop Condition

## Slide 21: I2C
Commonly Used For
  Sensors
  Control of multiple devices
  OLEDs
  Accelerometers
Advantages
  Widely used
  Requires only two wires
  Ack/Nack
  Multiple master/multiple slave
Disadvantages
  Fixed frame size
  Slower than SPI
  More complicated than SPI

## Slide 22: Other Serial Devices
USB ,PCIe, SATA, CAN

## Slide 23: Even More Serial Devices
Ethernet, HDMI, Coax (Digital Video), Display Port, Firewire

## Slide 24: Parallel Communication
Examples are PCI, PATA
  No longer favorable because of limits in speed
  Cable length
  Hardware complexity
However, is easy to implement on FPGA

## Slide 25: Parallel Communication & FPGAs
2-bits for message type/header
(eg. moved to new location; found treasure at square, etc.)
For example:
3-bits for message body
(eg. moved to square 4,5; square 7,7 is type wall, etc.)
1-bit for started, stopped mapping…
. and so on …
.
.

## Slide 26: Parallel Communication & FPGAs
wire inputs [n:0];
assign inputs = GPIO_0_D[m:0];
…
always @ (*) begin
if (inputs{1:0} == 2’d3) begin
grid_array[x][y] = inputs{5:2};
end
…
reg [2:0] grid_array [n-1:0][n-1:0];
wire [2:0] square_color;
assign square_color = GPIO_0_D[k:k-2];
…
always @ (*) begin
if (square_color == 3’d0) begin
grid_array[x][y] = square_color;
end
…
Plenty of ways to implement
(pseudocode):
msg header
msg body
Drawback: Consumes a lot of pins
Arduino sends color directly. Reserved GPIO pins specifically for color.
Arduino sends msg header {1:0} + body {5:2} indicating color change should take place at square x,y.

## Slide 27: Choosing a Protocol
Heavily dependent on what type of robot you want to build
Considerations
  Cost
  Usable wire length
  Device pin count
  Speed
  Etc.
You can also make your own communication protocol!

## Slide 28: References
Much of this presentation material is based on material discussed in www.circuitbasics.com
  SPI, UART, & I2C
Sparkfun also has excellent discussions on these topics